Fibre Channel

I/O Processor

Flash Utility User Guide

August 2000

Version 1.0

Document Number:

LSI Logic products are not intended for use in life-support appliances, devices,
or systems. Use of any LSI Logic product in such applications without written
consent of the appropriate LSI Logic officer is prohibited.

Document: Fibre Channel Flash Utility user Guide, First Edition (August 2000).

This document describes the software programming model for LSI Logic Corporation’s Fibre Channel I/O Processor products, and will remain the official reference source for all revisions/releases of this product until rescinded by an update.

To receive product literature, visit us at http://www.lsilogic.com.

LSI Logic Corporation reserves the right to make changes to any software described herein at any time without notice. LSI Logic does not assume any responsibility or liability arising out of the application or use of any product described herein, except as expressly agreed to in writing by LSI Logic; nor does the purchase or use of a product from LSI Logic convey a license under any patent rights, copyrights, trademark rights, or any other of the intellectual property rights of LSI Logic or third parties.

Copyright © 2000 by LSI Logic Corporation. All rights reserved.

TRADEMARK ACKNOWLEDGMENT

The LSI Logic logo design is a registered trademark of LSI Logic Corporation.

ARM is a registered trademark of Advanced RISC Machines Limited, used under
license. All other brand and product names may be trademarks of their respective companies.

Table of Contents

1	Installing FC Serial EEPROM Utility	4

1.1	Requirements	4

1.2	Installation Procedures	4

2	Executing FC Serial EEPROM Utility	5

2.1	Execution Without Command Line Arguments:	5

2.2	Execution with Command Line Arguments	6

2.1.2.1	Command Line Argument –bx	7

2.1.2.2	Command Line Argument –c	7

2.1.2.3	Command Line Argument –d	7

2.1.2.4	Command Line Argument –e	7

2.1.2.5	Command Line Argument –f	7

2.1.2.6	Command Line Argument –p	8

2.1.2.7	Command Line Argument –tx	8

2.1.2.8	Command Line Argument –vx	8

2.1.2.9	Command Line Argument –xy:	8

3	Menu Options	9

3.1	View SEEPROM Settings Menu Option	9

3.2	Identify Menu Option	10

3.2.1	Production Firmware Version Already Loaded	10

3.2.2	Firmware Version from a File	10

3.2.3	INT 13 BIOS Version from a File	11

3.3	Download Flash	12

3.3.1	Download Production Firmware to FLASH	12

3.3.2	Download INT 13 BIOS to FLASH	13

3.4	Upload Current FLASH to a File	13

3.5	Erase FLASH	13

3.6	Select PCI adapter to test	14

3.7	Quit	14

# Installing FC Serial EEPROM Utility

## Requirements

FC Serial EEPROM Utility is used with Intel Pentium based machines running MS DOS 6.22, or a DOS equivalent such as DR-DOS.

## Installation Procedures

Make a directory on your systems local hard drive.

(Example:  md c:\fcprom <ENTER>)

Copy FCPROM.EXE into that directory.

(Example:  xcopy a:\fcprom.exe c:\fcprom\*.* /v <ENTER>)

If you plan to program the Serial EEPROM with a text file, you may want to copy them to the directory where you placed FCPROM.EXE.

(Example: xcopy a:\mfginfo.txt c:\fcprom\mfginfo.txt /v <ENTER>)

# Executing FC Serial EEPROM Utility

The FC Serial EEPROM Utility is started by entering <fcprom> on the command line, with or without the command line arguments, described below.

## Execution Without Command Line Arguments:

A menu, similar to below will display all FC Host adapters detected by the System BIOS in your system:

|  | Vendor | Device |  |  |
| --- | --- | --- | --- | --- |
| Choice | ID | ID | Bus | Device |
| 1 | 1000h | 0621h | 0h | 68h |
|  | LSI Logic, Inc. SYMFC909 Fibre Channel Host Adapter |
| 2 | 1000h | 0621h | 0h | 70h |
|  | LSI Logic, Inc. SYMFC909 Fibre Channel Host Adapter |
| 3 | Refresh |  |  |  |
| Which chip (0 to quit)? |  |  |

Select which chip/board to update. Selection is made by entering the number (Choice),  specified on the left hand side of the menu, of the board you are using.

## Execution with Command Line Arguments

These are the valid command line arguments to FcProm:

-bx

Flash the BIOS where x is the name of the ROM image.  (filename is optional, default mptbios.rom).

-c

Changes the Class Code from 0x0e0001 t0 0x010000

-d

Change which adapter is currently in use.

-e

Erase the Flash

-fx

Flash the firmware where x is the name of the image.  (filename is optional, default fc909.rom)

-p

Display current protocol settings

-tx

Toggle protocol settings where x = 0 or 1.  (0 = Initiator/LAN   1 = Target / LAN)

-vx

Sets the SubsystemID and SubsystemVendorID where x is the value to be used. (ex: -v0xDEADBEEF, where 0xDEAD is the SubsystemID and 0xBEEF is the SubsystemVendorID)

-xy

Force 32bit data where y = 0 or 1.  (0 = Allow 32 or 64 bit data   1 = Force 32bit)

-?

Lists all valid options.

#### Command Line Argument –bx

The –b option downloads the BIOS binary image.  The ‘x’ argument specifies the name of the ROM image you want flashed.  (fcprom –bmptbios.rom)

The x argument is optional and a default of mptbios.rom will be used instead.

( fcprom –b)

#### Command Line Argument –c

The –c option changes the Class Code from the current value to 0x010000.  There will not be any text displayed to the screen.

#### Command Line Argument –d

The –d option changes which chip/board is updated (defaults to the first adapter).   A table (shown below) allows a chip/board to be selected.

|  | Vendor | Device |  |  |
| --- | --- | --- | --- | --- |
| Choice | ID | ID | Bus | Device |
| 1 | 1000h | 0621h | 0h | 68h |
|  | LSI Logic, Inc. SYMFC909 Fibre Channel Host Adapter |
| 2 | 1000h | 0621h | 0h | 70h |
|  | LSI Logic, Inc. SYMFC909 Fibre Channel Host Adapter |
| 3 | Refresh |  |  |  |
| Which chip (0 to quit)? |  |  |

Specify which chip/board to use. Enter the number (Choice) specified on the left hand side of the menu, of the board you which to use.

#### Command Line Argument –e

The –e option will erase the entire Flash.

#### Command Line Argument –f

The –f option updates the firmware.  The ‘x’ argument specifies the binary image to update.

(ex. fcprom –bfc909.rom)

The ‘x’ argument is optional and a default of fc909.rom will be used instead.

(ex. fcprom –f)

#### Command Line Argument –p

The –p option displays the current protocol settings.

Valid settings:

Logical Bus Addressing / FCP Initiator / LAN

FCP Target / LAN

#### Command Line Argument –tx

The -t option selects one of two protocals, using the argument ‘x’.

0 = Logical Bus Addressing / FCP Initiator / LAN

1 = FCP Target / LAN

#### Command Line Argument –vx

The -v option sets or resets the SubsystemID and SubsystemVendorID.  The ‘x’ argument specifies both the SubsystemID and the SubsystemVendorID, concatenated together as a single value:

-v0x(SubsystemID)(SubsystemVendorID)

example: -v0x11112222

#### Command Line Argument –xy:

The -x option sets the card to allow only 32bit PCI data transfers.  The ‘y’  argument may take the value 0 or 1.  The 0 = Allow 32 or 64 bit data, the 1 = Force 32bit.

# Menu Options

## View SEEPROM Settings Menu Option

This option displays the Serial EEPROM Hardware and Firmware settings on the chip.  A typical display screen is shown below.

HARDWARE SETTINGS

| SubsystemId | ………………………. | 0x010 |
| --- | --- | --- |
| SubsystemVendorId | ………………………. | 0x010 |
| ClassCode-Interface | ………………………. | 0x0e |
| ClassCode-SubClass | ………………………. | 0x00 |
| ClassCode-BaseClass | ………………………. | 0x01 |
| Shared Memory Size | ………………………. | 0x7 |
| Diagnostic Memory Size | ………………………. | 0x6 |
| PLL Configuration | ………………………. | 0x00 |
| Checksum | ………………………. | 0xc5 |

FIRMWARE SETTINGS

| FwFactoryVersion | ………………………. | 0x00000001 |
| --- | --- | --- |
| PortWWN[Hi-DW] | ………………………. | 0x100000a0 |
| PortWWN[Lo-DW] | ………………………. | 0xb8123456 |
| NodeWWN[Hi-DW] | ………………………. | 0x200000a0 |
| NodeWWN[Lo-DW] | ………………………. | 0xb8123456 |
| Chipname | ………………………. | SYMFC909 |
| ChipRev | ………………………. | N/A |
| BoardName | ………………………. | SYM40990 |
| BoardAssembly | ………………………. | 348-0037763c |
| BoardTracerNumber | ………………………. | C0400331099 |
| Checksum | ………………………. | 0xfa |

## Identify Menu Option

### Production Firmware Version Already Loaded

This option displays the current version of firmware installed on the chip.  A typical display is shown below.

Board Firmware Identification

***********************************************************************

FIRMWARE VERSION:

SYMFC909-2000.05.17	[  FLASH 909.B1  ]

### Firmware Version from a File

This option displays the version of firmware file on disk. A typical display is shown below.

File Firmware Identification

***********************************************************************

Enter name of the FLASH image:

Enter the name of the file and press enter.

SYMFC909-2000.05.17

[  FLASH 909.B1  ]

### INT 13 BIOS Version from a File

This option displays the version of BIOS from a file on disk.  After selecting this option you will see:

File BIOS Identification

***********************************************************************

Enter name of the INT13 BIOS (default = mptbios.rom):

Enter the name of the file and press enter.

Extracting information on Firmware image mptbios.rom: PCI-0.00.00.32(2000.05.17)

## Download Flash

### Download Production Firmware to FLASH

This option downloads firmware from a file to the chip.

Download Production Firmware to FLASH

***********************************************************************

FLASH image name (default fc909.rom):

Enter the name of the firmware file and press enter.

Found Source File and Opened

Validate Flash Rom?

USER NOTE: This is only for HDM Flash image (fcxxx.rom)

Y ………………………… yes

N ………………………… no

The selected firmware image may be optionally validated (recommended). If validation is selected, the following will be displayed.

Signature 1 is 0xXXXXXXXX

Signature 2 is 0xXXXXXXXX

Signature 3 is 0xXXXXXXXX

*** Flash signature VERIFIED! ***

CheckSum total is 0xXX

*** Flash checksum VERIFIED! ***

FLASH is initialized!

FLASH Status is cleared!

Write will start at block x (byte x) and end at block x.

Preparing to write xxx bytes

The utility will display the block number being written.

### Download INT 13 BIOS to FLASH

This option loads BIOS from a file to the chip.

This will program a BIOS image to FLASH.  Block 15 is the section of FLASH where the BIOS image will be programmed.  The starting byte of BIOS image will be at 0xFFFFF and will be programmed in reverse order (0xFFFFF – 0xF0000).  The remainder of the 64Kb block will be zeroed out.

***********************************************************************

Enter the Souce File for BIOS image (defult = mptbios.rom):

Enter the name of the file and press enter.

Erasing FLASH block 15

Preparing to write to FLASH …

Writing 0xXXXXXXXX at 0xXXXXX

## Upload Current FLASH to a File

This option will upload the current BIOS or Firmware binary image from FLASH to a file of your choice.

## Erase FLASH

This option will erase all blocks of the FLASH. Any resident BIOS or Firmware binary images will be erased.

## Select PCI adapter to test

This option selects another chip.

|  | Vendor | Device |  |  |
| --- | --- | --- | --- | --- |
| Choice | ID | ID | Bus | Device |
| 1 | 1000h | 0621h | 0h | 68h |
|  | LSI Logic, Inc. SYMFC909 Fibre Channel Host Adapter |
| 2 | 1000h | 0621h | 0h | 70h |
|  | LSI Logic, Inc. SYMFC909 Fibre Channel Host Adapter |
| 3 | Refresh |  |  |  |
| Which chip (0 to quit)? |  |  |

Enter the number specified on the left hand side of the menu.

## Quit

This option will exit the program.