## Slide 1
Metrology Of & Metrology Using
Single-Photon Detectors
NIST, Boulder, CO & Gaithersburg, MD & U. Maryland
  Rochester Institute of Technology, Rochester, NY , Nov 28, 2011
Alan Migdall
Sergey Polyakov
Jay Fan
Jun Chen
Zachary Levine
Elohim Becerra
Elizabeth Goldschmidt
Joffrey Peters
Natalia Borjemscaia
Boris Glebov
Bill Phillips
Paul Lett
Alberto Marino
Glenn Solomon
Edward Flagg
Andreas Muller
Sae Woo Nam
Rich Mirin
Thomas Gerrits
Shellee Dyer
Burm Baek
Brice Calkins
Adriana Lita
Jeff Van Lanen
Nathan Thomlin
John Lehman
Ming Ming Feng
Anna Fox
Mary Rowe
Manny Knill
Scott Glancy
Josh Bienfang
Allesandro Restelli
Christoph Wildfeuer, LSU
Ivo Degiovanni, INRIM
Kevin Silverman
Martin Stevens
Matthew Eisaman, Brookhaven
Alexander Ling, NUS
Aaron Pearlman, NOAA
Sarah Beavan, ANU
Valentina Schettini, MIT
David Branning, Trinity Col.
Michael Ware, BYU
William Kelly, SJC
Colin McCormick
David Papoular, ENS

## Slide 2: Metrology Of and Metrology Using Single-Photon Detectors
Given the tiny energies involved, the generation and detection of one photon at a time is an extraordinary feat. Even with this difficulty, the development of single-photon technology is rapidly advancing. Because this technology involves dealing directly with individual quantum states, it opens up many areas that push the conventional limits, and thus is a strong motivation for this development. One big driver has been the field of quantum information which offers the potential of nothing less than revolutionizing our abilities to calculate here-to-fore intractable calculational problems, to test fundamental principles of the nature, to provide communication where absolute security is based on fundamental physical principles, and to make measurements beyond what are fundamental limits in the classical world. With all this potential, it is no wonder there is such interest in improving single-photon devices.
I will review single photon detector and source technology and some applications. One area of particular interest to us at NIST is their use in metrology. I will present techniques that use this technology for measurements that are not possible any other way and to, in turn, use the techniques made possible by these devices, to characterize the devices themselves. I will also discuss their use in a fundamental test of nature.
abstract

## Slide 3
Outline
Overview of Single-Photon Detector & Source Technology
Applications of Single-Photon Technology
stuff only possible with single-photon tools
accuracy only possible with single-photon tools
  Quantum Information
    Quantum cryptography
    Quantum computation
  Metrology
    Radiometric measurements of
      sources, detectors, sources by detectors, detectors by sources by detectors
    Position measurements
  Fundamental test
  Future

## Slide 4: Who cares about single-photons?
Fluorescence Lifetime Imaging
Time resolved single-molecule spectroscopy
Near-field optical microscopy
Light detection and ranging (LIDAR)
Astronomy
Medical diagnostics
Interplanetary communication
Quantum Information
  Computing
  Cryptography
…….
Entanglement

## Slide 5
Single Photon Interest

## Slide 6
Single Photon?
Visible to Near Infrared
(400 - 1700 nm)
@ l = 1000 nm
Energyphoton ~2x10-19 joules
1 W = 5x1019 photons/second
(Luminous efficiency ~ 2 to 10%)
Energyphoton = h ×n = h × c /l
100 W bulb  2 W light

## Slide 7: How small are we talking?
E = 2x10-6 joules
http://www.hhs.state.ne.us/puh/epi/wnv/links.htm
g
10 cm
~2 mg
Ephoton(l=1550 nm) ~1.3x10-19 joules
Compare to Mosquito?
1 = 1.6x1013

## Slide 8: How to Detect? Photoelectric Effect
e-
hn
Hertz 1887
Einstein 1905
Current
How to detect
a single e- ?

## Slide 9: Photomultiplier Tube
1 e- in  106 e- out
The Secondary Emission Phototube
H. Iams and B. Salzberg, Proc. IRE 23, 55 (1935).
The Secondary Emission Multiplier-A New Electronic Device
V. Zworykin, G. Morton, and L. Malter, Proc. IRE 24, 351 (1935).
Multiple Amplifier
L. A. Kubetsky, Proc. Inst. Radio Eng. 254, 421 (1937).
First Single-Photon Counting:
K. O. Kiepenheuer, Z. Phys. 107, 145 (1937).
Z. Bay, Nature (London) 141, 1011 (1938).
J. S. Allen, Phys. Rev. 55, 966–971 (1939).
Notes: History ref with reference to
Author’s certificate #24040, priority 4 August 1930 :
http://arxiv.org/ftp/physics/papers/0601/0601159.pdf

## Slide 10: Single-Photon Avalanche Photodiode
Vbias
APD
Rload
1960s

## Slide 11: Fundamental Limit How much gain to do you need? How small an electrical pulse can you reliably sense?
Assume:
  Detector capacitance » 1 pF
  Detection Bandwidth » 10 GHz
 RloadCDet » 100 ps  Rload » 100 W
Johnson noise
» 0.1mV (at R=50 W, T=300K)
Vbias
APD
Rload
J. Bienfang
Vn = Ö 4kBTRDf
Want low dark count rate » 10-5 dark count /ns
(thermal fluctuation < photon signal)
 threshold at 5x Johnson noise » 0.5mV (104 e-)

## Slide 12: Detectors
RSI Source & Detector Review 82, 071101 (2011)
Photomultiplier tube
Single Photon Avalanche photodiode
  Visible- Silicon
    thick junction
    thin junction
    self differencing
    linear mode
    cavity
    Multipixel
  Infrared
    Gated
    Self differencing
    Discharge pulse
Hybrid
  PMT & APD
  Time multiplexed
  Space multiplexed
infrared- InGaAs

## Slide 13: Detectors
RSI Source & Detector Review 82, 071101 (2011)
Photomultiplier tube
Single Photon Avalanche photodiode
  Visible- Silicon
    thick junction
    thin junction
    self differencing
    linear mode
    cavity
    Multipixel
  Infrared
    Gated
    Self differencing
    Discharge pulse
Hybrid
  PMT & APD
  Time multiplexed
  Space multiplexed
infrared- InGaAs
niobium nitride
4 nm

## Slide 14: Transition Edge Sensor (TES) Microbolometer
Absorber, C
Thermometer
Weak thermal link, g
Thermal sink
(50 mK)
Energy
deposition
T
R
Rn
S. Nam
It Can Really Count Photons
Optimized for photon-number resolution, not speed (trise~100 ns, tfall~1 ms)
Absorption events show good distinguishability
Much slower than APDs
Energy Resolution = 2x10-20 J !
Wavelength Efficiency
1550 nm ~ 95%
800 nm ~ 99%
Photon #
Counts

## Slide 15: Transition Edge Sensor: pushing the limits
Rs ~ 10 mW
Rp
RTES
I
R
T
Rn
t
I

## Slide 16: Beyond Single Photon Counting Temporal Traces
signal (arb. units)
signal (arb. units)
~5,000,000 photons
50,000 photons
R
T
Rn
t
Rs ~ 10 mW
Rp
RTES
I
I

## Slide 17: Width uncertainty determination
Measured 100 photons
with 3 photons uncertainty
and 94 % quantum efficiency
x

## Slide 18: Sources
Laser

## Slide 19
Optical Parametric Downconversion
One in - two out
Creating light two photons at a time

## Slide 20
Optical Parametric Downconversion

## Slide 22
Two-photon light
c(2) parametric down-conversion
  One photon in – two photons out
lpump= 351 nm

## Slide 23
Different
Crystal
Tilts
Produce
Different
Output
Patterns

## Slide 25
l
l
Calc.
PDC displaying its own phase matching curve

## Slide 26
Laser
Attenuator
Pulsed Laser
First step to On-Demand production
Single Photons only during pulse, but still not really On-Demand
fixes random
arrival problem
< 1 photon/pulse
“Heralded” photons

## Slide 27
P1
P1
Problem of getting just one
Probability of producing a photon or a pair must be small
Laser

## Slide 28
~ 10% produce a photon pair
Train of N single photons
On demand
Pulsed Pump Laser
Optical Cross Connects
& Delays
Toward a True Single-Photon Source:
Multiplexed PDC
Separates
P1 from P>1
Which one information

## Slide 29
Outline
Overview of Single-Photon Detector & Source Technology
Applications with Single-Photon Technology
stuff only possible with single-photon tools
accuracy only possible with single-photon tools
  Quantum Information
    Quantum cryptography
    Quantum computation
  Metrology
    Radiometric measurements
      Sources, detectors, sources by detectors, detectors by sources by detectors
    Position measurements
  Fundamental tests
  Future

## Slide 30: Why the interest?
Quantum Information
A convergence of two of the 20th Century’s great revolutions
Information
(i.e. books, data, pictures)
More abstract
Not necessarily material
Quantum Mechanics
(i.e. atoms, photons, molecules)
“Matter”
Quantum Information- via the Superposition Principle:
one N-qubit register can store all 2N numbers!
300 Qbits = 1090 - more than all the atoms in the universe!
A quantum computer if it existed could break all present- day public key encryption systems
Quantum encryption can defeat any computational attack

## Slide 31: Scaling of Quantum Information
Classically, information stored in a bit register: a 3-bit register stores one number, from 0 – 7.
0
1
0
Quantum mechanically, a 3-qubit register can store all of these numbers in an arbitrary superposition:
Result:
  Classical: one N-bit number
  Quantum: 2N (all possible) N-bit numbers
20
21
22
1
1
1
0
0
0
1
0
0
0
1
0
e.g.
…
1
1
0
300 Qbits = 1090 - more than all the atoms in the universe!

## Slide 32
Quantum Cryptography–
Alice and Bob need
identical but random keys
Physically Secure- Secrecy depends on Laws of
Quantum Mechanics not
a hard calculation
A
l
i
c
e
'
s
b
i
t
v
a
l
u
e
1
0
0
0
1
1
A
l
i
c
e
'
s
p
o
l
a
r
i
z
a
t
i
o
n
B
o
b
'
s
p
o
l
a
r
i
z
a
t
i
o
n
b
a
s
i
s
B
o
b
'
s
r
e
s
u
l
t
1
1
0
0
1
1
S
a
m
e
b
a
s
i
s
?
Y
N
N
Y
N
Y
T
r
a
n
s
m
i
t
t
e
d
k
e
y
1
0
1
A
l
i
c
e
'
s
s
i
n
g
l
e
p
h
o
t
o
n
s
o
u
r
c
e
a
n
d
p
o
l
a
r
i
z
a
t
i
o
n
s
e
l
e
c
t
o
r
B
o
b
'
s
p
o
l
a
r
i
z
a
t
i
o
n
a
n
a
l
y
z
e
r
s
p
i
c
k
0
o
r
1
a
n
d
p
i
c
k
a
b
a
s
i
s
p
i
c
k
a
b
a
s
i
s
&
m
e
a
s
u
r
e
t
h
e
n
c
h
e
c
k
A
l
i
c
e
'
s
b
a
s
i
s
v
i
a
c
l
a
s
s
i
c
a
l
c
h
a
n
n
e
l
T
w
o
B
a
s
i
s
s
e
t
s
(
a
l
p
h
a
b
e
t
s
)
}
B
B
8
4
P
r
o
t
o
c
o
l
Quantum Channel
Single photon link

## Slide 33: What does quantum crypto add? (disclaimer)
Classical | Quantum
Security depends on hiding large prime factors in really big numbers: “Computational Security” | Security depends on quantum mechanics laws being true: “Physical Security”
Finding large factors of large number is hard today | Physical laws are true today and tomorrow
But… Mathematics has not proven that factoring must be hard | But… this is a belief that cannot be proved the way a mathematical theorem can

## Slide 34
Physical Measurement Laboratory
Josh Bienfang
w/ A. Restelli, J. Galang, A. Migdall, C.W. Clark
X. Tang(ITL), A. Mink(ITL)
High-speed single-photon signaling

## Slide 35
Heralded Pulse/Gate
DARPA QuIST QKD Testbed
Testbed for high-speed quantum key distribution
  Si detectors  Free-space link
0.8 nsec
Synchronization: 8b/10b encoding/clock recovery
1.25 Gb/s classical channel defines 0.8 ns gates
Limited by detector jitter and recovery time
Fastest free-space QKD (… known)
850nm VCSELs
Si APDs
Quantum channel
Classical channel

## Slide 36
The view from Bob

## Slide 37
Histogram of single-photon arrival times at 1.25 GHz
 Quantum bit error rate due to detector jitter
<1% @ 1.25 GHz
1.25 Gbps clock
from Alice
1.25 Gbps optical from Alice – Gain switched VCSELs
Detector Timing Jitter Issue at 1.25 GHz
Collaboration w/
S. Cova et al. at
Politecnico di Milano
60 ps FWHM
380ps FWHM
1.3ns FW1%M
160ps FWHM
590ps FW1%M

## Slide 38: Application: Time-Correlated Single-Photon Detection
Fiber
SSPD
Cryostat
Mono-
chromator
@ 780 nm
82 MHz
Detector | IRF (FWHM) | Efficiency @ 900 nm | Dark Counts
Conv’l SPAD | 350 ps | 38% | ~50 Hz
Fast SPAD | 40 ps Long tail | 5% | ~50 Hz
SNSPD | 65 ps Gaussian | 2% | <30 Hz
Gaussian response + Few dark counts
→ Tolerate low efficiency
→ Identify multiexponential processes
Timing Electronics
Stop
Start
Stevens et al., APL 89, 031109 (2006)
Sample
Ti:Sapphire
Laser
1 ps, 780 nm
BS
Dichroic
BS
780 nm
>780 nm
Fast Photodiode (Si)
SNSPD
Notes: 38

## Slide 39
Outline
Overview of Single-Photon Detector & Source Technology
Applications with Single-Photon Technology
stuff only possible with single-photon tools
accuracy only possible with single-photon tools
  Quantum Information
    Quantum cryptography
    Quantum computation
  Metrology
    Radiometric measurements
      Sources, detectors, sources by detectors, detectors by sources by detectors
    Position measurements
  Fundamental tests
  Future

## Slide 40
Detector to be Calibrated
Trigger or “Herald” Detector
Two-Photon Detector Efficiency Scheme
No External Standards Needed!

## Slide 41
Absolute Radiometric Source Standards
Black Body
Synchrotron
Correlated Photon Source

## Slide 42
DUT
Trigger
Verifying the Method
w
0
w
2
P
A
R
A
M
E
T
R
I
C
C
R
Y
S
T
A
L
C
O
U
N
T
E
R
C
O
I
N
C
C
O
U
N
T
E
R
A
b
s
o
l
u
t
e
Q
u
a
n
t
u
m
E
f
f
i
c
i
e
n
c
y
C
O
U
N
T
E
R
N
Calibrated
Si Detector
A
b
s
o
l
u
t
e
Q
u
a
n
t
u
m
E
f
f
i
c
i
e
n
c
y
Comparison

## Slide 43
Sources of uncertainty:
DUT Collection Efficiencies
Spatial
Angular
Spectral
…
Turning Two-Photon Method
into Metrology
Trigger counting
Coincidence determination

## Slide 44: Method agreement and confidence bands
Δ

## Slide 45: Comparison/Results
NIST implementation of High Accuracy SPD Calibration methods
Uncertainty of each individual comparison:
0.25%
Overall mean difference between the two methods:
0.15%0.14% (h sub. > h 2-photon)
Highest accuracy verification of the 2-photon method yet achieved
Method | Absolute uncertainty
Two-photon | 0.18%
Substitution | 0.17%

## Slide 46: 2-Photon Metrology Progress
Year | 1st author | Uncertainty of |  | External Comparison
 |  | Method | Verification | 
1970 | Burnham | ~35% |  | Calibrated lamp
1981 | Malygin | - |  | 
1986 | Bowman | ~10% |  | 
1987 | Rarity | ~10% |  | HeNe + attenuation
1991 | Penin | > 3% |  | 
1993 | Ginzburg | ~10% |  | Published values
1994 | Kwiat | ~3% |  | 
1995 | Migdall | < 2% | 1% | Calibrated Si Detector
2000 | Brida | ~0.5% | 2% | Calibrated Si Detector
2005 | Ghazi-Bellouati | 1.1, 0.62% | 6.8% | French cryoradiometer
2006 | Wu | 2.1% |  | 
2006 | Polyakov | 0.18% | 0.15% | Calibrated Si Detector

## Slide 47: Metrology Progress
Our work

## Slide 48: Metrology plans
Moving high accuracy from lab to users
Connecting:
  many-photon radiometry
  to
  single-photon radiometry
Issue: 1 watt ~ 1019 photon/s

## Slide 49: Number-Resolving Detectors & Nonclassical Sources: Tools for Enhanced Measurement
PNR
49
Is enhanced measurement capability possible with just Number-Resolving Detectors?
(motivation: simpler to implement than using both)
Length & Spectral Resolution tested with Fabry-Perot Transmittance Spectrum
Spatial Resolution tested by resolving two adjacent beams
PNR
Two spots with
better contrast with PNR
Better Resolution with PNR:
transmittance structure allows
better position determination
n=4
Fock state
Coherent
state

## Slide 50: What additional enhancement is gained with Nonclassical Sources?
Gaussian profile
Mean photon number =10
Number-resolved profile
coherent
thermal
Fock, N=10
k=10
k=1
50
Effects of photon source statistics on beam compression?
Fock State source wins but, number-resolved detection with coherent state beats
“classical” detection
Number-resolved
spatial profiles

## Slide 51
Outline
Overview of Single-Photon Detector & Source Technology
Applications with Single-Photon Technology
stuff only possible with single-photon tools
accuracy only possible with single-photon tools
  Quantum Information
    Quantum cryptography
    Quantum computation
  Metrology
    Radiometric measurements
      Sources, detectors, sources by detectors,
      detectors by sources by detectors
    Position measurements
  Fundamental tests
  Future

## Slide 52: Chaotic, Pseudo-Thermal Source
Fast Photodiode
Fiber
CW Diode Laser
1070 nm
Time-Dependent
Speckle
Oscilloscope
Rotating Ground Glass
Polarizer
Ideal Single-Mode Chaotic Source
g(2)(0) = 2 g(n)(0,0,…0) = n!
g(3)(0,0) = 6 g(4)(0,0,0) = 24
Notes: 52

## Slide 53: 2nd-Order Coherence
PC
4-Channel
Time-Tagging Electronics
4-element
SNSPD
Closed-Cycle
Cryostat
Rotating Ground Glass
Fiber
CW Diode Laser
1070 nm
Time-Dependent
Speckle
g(2)(0) = 1.985 ± 0.019
Polarizer
Ideal Single-Mode Chaotic Source
g(2)(0) = 2 g(n)(0,0,…0) = n!
g(3)(0,0) = 6 g(4)(0,0,0) = 24
ND
Multiple detectors allows t=0 measurements
Notes: 53

## Slide 54: 2nd-Order Coherence
Chaotic
Source
PC
4-Channel
Time-Tagging Electronics
4-element
SNSPD
Fiber
CW Diode Laser
1070 nm
Closed-Cycle
Cryostat
Mirror
Coherent Source (Laser)
Ideal Coherent Source
g(2) = 1 g(n) = 1
ND
Notes: 54

## Slide 55: Higher-Order Coherence
2
6
Chaotic
Source
g(4)
g(3)
g(2)
PC
4-Channel
Time-Tagging Electronics
4-element
SNSPD
Fiber
CW Diode Laser
1070 nm
Closed-Cycle
Cryostat
Mirror
Coherent Source (Laser)
ND
Notes: 55

## Slide 56: Higher-Order Coherence
2
6
 | Expected | Result | Expected | Result
g(2) | 1 | 1.0018 ± 0.0008 | 2 | 1.99 ± 0.02
g(3) | 1 | 1.006 ± 0.002 | 6 | 5.9 ± 0.2
g(4) | 1 | 1.011 ± 0.005 | 24 | 23 ± 2
Coherent (Avg)
Coherent Source
(Laser)
Chaotic
Source
g(4)
g(3)
g(2)
Chaotic (All ti = 0)
Notes: 56

## Slide 57: 3rd-Order: Chaotic Source
g(3)(0,0) = 5.87±0.17
Ridges:
g(3) ≈ 2
Uncorrelated: g(3) ≈ 1
Data
Notes: 57

## Slide 58: 3rd-Order: Chaotic Source
g(3)(0,0) = 6
Ridges:
g(3) = 2
Uncorrelated: g(3) = 1
Theory
Calculation assumes ideal Gaussian scattering process:
P.-A. Lemieux and D. J. Durian, JOSA A 16, 1651 (1999)
Notes: 58

## Slide 59: 3rd-Order: Coherent Source
Data
Mean value: <g(3)> = 1.006 ± 0.002
→ Precision measurement of weak cross-correlation
Notes: 59

## Slide 60: 4th-Order: Chaotic Source
t3 = -5 ms
t3 = -3 ms
2 at one time, 2 at another time g(4) ≈ 4
All 4 at different times g(4) ≈ 1
t3 = -1 ms
t3 = 0
All 4 at once: g(4)(0,0,0) = 23.1±1.8
t3 = +1 ms
t3 = +3 ms
t3 = +5 ms
2 Elements fire simultaneously
g(4) ≈ 2
3 at once
g(4) ≈ 6
Notes: 60

## Slide 61
Outline
Overview of Single-Photon Detector & Source Technology
Applications with Single-Photon Technology
stuff only possible with single-photon tools
accuracy only possible with single-photon tools
  Quantum Information
    Quantum cryptography
    Quantum computation
  Metrology
    Radiometric measurements
      Sources, detectors, sources by detectors, detectors by sources by detectors
    Position measurements
  Fundamental tests
  Future

## Slide 62: Ontology
Ontology (from the Greek nominative ὤν: being, genitive ὄντος: of being (participle of εἶναι: to be) and -λογία: science, study, theory) is a study of conceptions of reality and the nature of being. In philosophy, ontology is the study of being or existence and forms the basic subject matter of metaphysics. It seeks to describe or posit the basic categories and relationships of being or existence to define entities and types of entities within its framework. It is the science of what is, of the kinds and structures of the objects, properties and relations in every area of reality.
Ontology has one basic question: "What exists?" Different philosophers provide different answers to this question.
What is existence? Is existence a property? What does it mean to say something does not exist? Is existence properly a predicate? Are sentences expressing the existence or non-existence of something properly called propositions?
What is an object? Can one give an account of what it means to say that an object exists?
The concept of ontology is generally thought to have originated in early Greece. Before Socrates, questions of being, stasis and change occupied Parmenides and Heraclitus. Parmenides is associated with the view that being must be affirmed and non-being avoided and denied. This is also expressed by Parmenides in the dictum "ἔστι γὰρ εἶναι" or "It is, namely, being."
Despite the seeming straightforwardness of the realist position, in the history of philosophy there has been continuous debate about what is real. In addition, there has been significant evolution in what is meant by the term "real".
Ontology (from the Greek nominative ὤν: being, genitive ὄντος: of being (participle of εἶναι: to be) and -λογία: science, study, theory) is a study of conceptions of reality and the nature of being.
Ontology has one basic question: "What exists?" Different philosophers provide different answers to this question.
What is existence? Is existence a property? What does it mean to say something does not exist?
What is an object? Can one give an account of what it means to say that an object exists?
The concept of ontology is generally thought to have originated in early Greece. Before Socrates, questions of being, stasis and change occupied Parmenides and Heraclitus. Parmenides is associated with the view that being must be affirmed and non-being avoided and denied. This is also expressed by Parmenides in the dictum "ἔστι γὰρ εἶναι" or "It is, namely, being."
Despite the seeming straightforwardness of the realist position, in the history of philosophy there has been continuous debate about what is real. In addition, there has been significant evolution in what is meant by the term "real".
2500 years ago…

## Slide 63: c. 2500 years later….

## Slide 64
measurement
setting
Measurement
result
-1 or 1
A
B
rewriting A1B1 + A1B2 + A2B1 - A2B2 ≤ 2
so A1 (B1 + B2) + A2(B1 - B2 ) ≤ 2
b
a
Locality means that either B1 + B2 or B1 - B2 must equal zero independent of
a
Bell test hand waving:
classically impossible correlations
1 or 2
can be measured with instrument set to 1 or 2, and will result in an output of -1 or 1
a
Hidden variable means that & have predetermined values for each of the measurements
b
a
-1
-1
1
-1
Measurements exceed 2
so local hidden variable is ruled out !

## Slide 65: Fundamental Problem: How does the world work?
Bell’s theorem and experimental tests
  Realism + Locality Þ Quantum Phenomena
Realism & Locality ?
How about Realism + Nonlocality ?
  Leggett’s theorem and experimental tests
  Realism + Nonlocality Þ Quantum Phenomena
2003-2007
1935-…
Realism  Hidden Variable

## Slide 66
Perhaps Hidden Variables that are Nonlocal ?

## Slide 67
Results using
PDC-based source
FWM-based demonstrated too

## Slide 68: Future
Detectors
  Efficiency
  Timing jitter
  Scalability
Sources
  Efficiency
    Extraction
    Generation
  State accuracy
Applications
  Quantum enhanced measurements
  Metrology of & using nonclassical tools
  Fundamental tests
We are always interested in collaborations, students, & postdocs.
(migdall@nist.gov)